## Slide 1: Gaussian Sampling Based Lattice Decoding
Bragadeesh (EE14B114)
Nived Rajaraman (EE14B040)
Dheeraj.M.Pai (EE14B082)

## Slide 2: MIMO system

## Slide 3: Channel model
, , fading gain channel
, , where is set of information symbols , sent vector
, , i.i.d Gaussian noise
, , received vector

## Slide 4: Simplified equation
,
, , where is set of information symbols
,
,

## Slide 5: The problem
This is identical to the lattice problem
which is NP-HARD!!!!! 

## Slide 6: Lattice decoding algorithm
Assume all entries of except at index is known
Sample randomly from it’s probability distribution
Expected to converge to the optimal solution at infinity
May not give optimal results with negligible probability

## Slide 7: Lattice decoding algorithm
where , is column of matrix

## Slide 8: Visualizing GSLD
At next iteration, new coordinate is chosen
  from the particular dimension instead of all points.
Conditional distribution along each dimension
  is known.
Expected to converge probabilistically to
  ML solution

## Slide 9: Implementation Specific Details
Discussing pseudo code, computational complexity and convergence

## Slide 10: Pseudo code
For every bit in the vector :
Generate = ỹ(i) = ŷ + hixi
  ŷ is the residual error :
Generate
Sample from ∼ and quantize to alphabet ()
Update with and update ŷ (residual error). Repeat from (1)
Convergence based on S
  S : # consecutive iterations the best solution has not changed
  : # iterations where best error is below threshold
  and : # max. number of iterations after which the
  unchanged estimated best solution is printed

## Slide 11: Restarts
Since the algorithm is probabilistic, in terms of both initialization as well as in iteration, the expected output follows a probability distribution.
To compensate for erroneous estimated vectors due to non-convexity of the problem, the algorithm is repeated with different starting vectors and the best solution is chosen based on the residual error of the estimated solutions as:
= arg

## Slide 12: vs. number of restarts (ML solution)
Image courtesy : T. Datta, A. Chockalingam, E. Viterbo, “Gaussian Sampling Based Lattice Decoding”

## Slide 13: Complexity
Max # iterations is heuristically chosen to be . In implementation, the constant is chosen as 16.log2|A|
Complexity per iteration: - Due to vector-vector dot products
# of updates/iteration is - each (of n) bit needs to be updated
Overall computational complexity of algorithm :

## Slide 14: Convergence
As σ->0, the solution does not converge to the optimal solution. The algorithm becomes deterministic (except for the random initialization), but the expected solution does not converge to the optimal
As σ becomes very large, the algorithm in principle would take a significant number of iterations to converge. This would be because the noise variance becomes significant to the distance between symbols and hence, the sampling and quantization step would not generate the same result over iterations with high probability.

## Slide 15: BER vs. SNR 16 x 16 16 QAM
log10(BER)
SNR ->
Solution is non-optimal: hence it does not converge to the
X = H-1y solution as σ -> 0

## Slide 16: BER vs SNR 32 x 32 16 QAM
log10(BER)
SNR ->
Solution is non-optimal: hence it does not converge to the
X = H-1y solution as σ -> 0

## Slide 17: Comparison with other models
Exact algorithms : ML decoding (Sphere decoder)[2].
Sub – optimal algorithms : K-best sphere decoding algorithm.
Fixed complexity sphere decoder
Randomized lattice decoding[Shuiyin et.al][4].
Other randomized algorithms [3].
[2]E. Viterbo and J. Boutros, “A universal lattice code decoder for fading channels,”
[3]T. Datta, N. A. Kumar, A. Chockalingam, and B. S. Rajan, “A novel MCMC algorithm for near-optimal detection in large-scale uplink multiuser MIMO systems,”
[4]S. Liu, C. Ling, and D. Stehle, “Randomized lattice decoding: Bridging the gap between lattice reduction and sphere decoding,”

## Slide 18: Comparison with other models
Complexity :
ML Decoder(Sphere decoder) : Exponential Complexity. Not feasible for higher dimensions.

## Slide 19: Comparison with other models
Complexity and SNR to achieve BER 0.01

## Slide 20: Comparison with other models
Complexity and SNR to achieve BER 0.01
GSLD > R-MCMC > FSD

## Slide 21: Comparison with other models
Performance:
ML Decoder > GSLD > R-MCMC > FSD

## Slide 22: BER vs SNR curve for 4QAM and 16-QAM
Image courtesy : T. Datta, A. Chockalingam, E. Viterbo, “Gaussian Sampling Based Lattice Decoding”

## Slide 23: BER vs SNR curve for 16QAM and 64-QAM
Image courtesy : T. Datta, A. Chockalingam, E. Viterbo, “Gaussian Sampling Based Lattice Decoding”

## Slide 24: Conclusion
The proposed GSLD performs competitively with the other existing models with much lower decoding complexity.
The algorithm is much easier to implement as compared to other lattice decoding algorithms

## Slide 25: References
[1]T. Datta, A. Chockalingam, E. Viterbo, “Gaussian Sampling Based Lattice Decoding”
[2]E. Viterbo and J. Boutros, “A universal lattice code decoder for fading
channels,”
[3]T. Datta, N. A. Kumar, A. Chockalingam, and B. S. Rajan, “A novel
MCMC algorithm for near-optimal detection in large-scale uplink
multiuser MIMO systems,”
[4]S. Liu, C. Ling, and D. Stehle, “Randomized lattice decoding: Bridging
the gap between lattice reduction and sphere decoding,”